## Slide 1: Playground Care
Sacramento City USD

## Slide 2: Our playgrounds!
Following assessment done on all playgrounds, Facilities will categorize them for future replacement.
SIA’s CPSI and ADA team is available to assist Risk Mgmt and Facilities with inspections and on replacement projects.
M&O will continue to address immediate repairs needed before school year resumes.
Work orders are promptly addressed on unsafe findings.
SIA will continue to schedule yearly Spring and Fall inspections, and custodial staff are required to do routine playground checks throughout the year.

## Slide 3: Custodian Role
Important role in daily update and keeping children safe
Daily:
  Rake exit areas of slides and under monkey bars
  Make sure footings of structure are not exposed
  Visual inspection EACH DAY
Monthly:
  Complete checklist
  Look for missing bolts, cracks, loose components, vandalism, environmental issues
  Send copy to Risk Management

## Slide 4: California Regulations
Since 2000, all public playgrounds were required to meet California regulations
All playgrounds must comply with:
  California Health & Safety Code, Section 115725-115735
  ASTM standards: F1487, F1292, F1951
  U.S. Consumer Product Safety Commission (CPSC) Handbook for Public Playgrounds #325
  2022 California Building Code Chapter 11B accessibility standards and 2010 ADA Standards for Accessible design

## Slide 5: Why is Maintenance Important?
Poor maintenance of equipment is cited as the second leading factor in playground injuries after improper use/poor supervision
79% of all playground injuries are due to falls

## Slide 6: Purpose of inspections
Safety – ensure safety of users
Function – keep equipment operational
Aesthetics – clean, attractive and sanitary
GOAL: Be proactive, not reactive

## Slide 7: Inspections
Daily – visual
Weekly – check fall material
Monthly – check equipment
Annually - fall material refills
Document all inspections!
  If it isn’t written down, it didn’t happen
  Take credit for the work you are doing!

## Slide 8: Recognizing hazards: Container box
Low fall material
Debris in box
Trip hazards
Damage and wear to box structure

## Slide 9
Height of slide exit to protective surfacing shall not be:
More than 11 inches if the slide height is 4 feet or less OR
Between 7 and 15 inches if slide height is great than 4 feet.

## Slide 10
24”

## Slide 11
Exposed footings indicate low loose protective surfacing material

## Slide 12
Exposed weed barrier material indicates low loose protective surfacing

## Slide 13
Weeds and other organic growth indicates lack of maintenance

## Slide 14
Watch for loose connections and exposed damage on container box materials.

## Slide 15
Repair torn unitary surfacing early to prevent further damage

## Slide 16: Recognizing hazards: Equipment
Damaged equipment
  Vandalism or missing components
Metal surfaces
  Sharp edges
Moving parts
  Worn “S” hooks
Hardware
  Protruding bolts
  Missing or loose hardware

## Slide 17
Watch for missing hardware

## Slide 19
Protruding bolts can create entanglement hazards and cause potential injury

## Slide 20
Open S-Hooks or other connections can cause equipment to become loose and disengaged as well as entangle clothing

## Slide 21
Missing equipment creates additional hazards. Block openings and close off all hazardous areas of the playground until repair or replacement is complete.

## Slide 22: Contact the district for…
Major damage
Replacement of components
Changes to equipment
Planned purchase of new equipment
  ADA compliance

## Slide 23: Playground Resources
Visit SIA’s YouTube channel to view the video Conducting a Routine Playground Inspection
  https://www.youtube.com/watch?v=uEyfYvits_s
SIA’s FREE playground warning labels:
  https://www.sia-jpa.org/materials-order/

## Slide 24: Thank you for keeping our kids safe!